## Slide 1
NTUT AIOT LAB · PROGRESS REPORT · AUGUST 2026
Following a Named Object
with Vision and Language

## Slide 2
Comparison
Last report's pilot.
Same guardrail, same simulator, same policy files — the pilot changed.
01
Before (AerialVLA 7B)
Now (this report)
Follow a named moving object
no — never moved
yes
Language actually steers
no
yes
Decision rate
0.11 Hz
4–5 Hz
Altitude band held
escaped 31.6 s
0.0 s
No-fly zone
0.0 s
0.0 s
Source: docs/FINDING-what-drives-aerialvla.md, docs/RESULT-vlm-follow.md

## Slide 3
THE FINDING
AerialVLA's language
108 controlled forward passes per adapter, on real captured frames.
02
12 / 12
flights: identical 'stop and land' output
0.05 vs 0.08
yaw for correct vs WRONG colour word
11 / 18
frames answered LAND with no compass hint
The prompt has two slots. Only one of them steers.
"Fly {direction} and find the target. {object}"
{direction} is a compass phrase computed from ground-truth coordinates — it orders the commanded
yaw monotonically from −0.47 rad/s ("to your left") to +0.16 ("to your right").
{object} is the language. Correct and wrong colour words gave indistinguishable actions.

## Slide 4
THE FIX
Change the model
Still vision → language → action. Now with a model whose words reach the output.
03
OWL-ViT 153 M
Open-vocabulary detector.
Text in, boxes out.
34–56 ms per frame.
Servo controller
Box offset → yaw.
Box width → speed.
Altitude error → climb.
Guardrail — unchanged
Same Shield, same policies.
No modification needed to
accept a new kind of pilot.
Nothing in the steering path knows where the car is. Its position is used only to spawn it,
and offline, to score the flight.

## Slide 5
THE DEMO
Two flights.
.\run_follow_vlm.ps1
04
1 · Tracking, with stops
The car drives, stops for 6 s, drives,
stops, drives again. The drone has to
stop too — that is the proof.
2 · The same, with a no-fly zone
A fence spans the corridor. The car
drives through it. The drone brakes,
holds at 3 m, and does not.
Recorded from two cameras: the drone's own view with the detection box and live telemetry,
and a third-person chase view, stitched side by side.

## Slide 6
RESULTS
It follows, and the rules hold.
Car at 2.0 m/s. Separation measured against its true position, offline.
05
Condition
Detector hit
Mean sep.
Within 30 m
Shield overrides
NFZ time
Follow: car stops twice
100%
15.6 m
100%
0
0.0 s
Follow + no-fly zone
67.8%
45.2 m
28.6%
0
0.0 s
Control: wrong colour
99.0%
68.5 m
20.7%
27
0.0 s
Row 1: the drone stops when the car stops — 1.17 m/s while the car moves against 0.36 m/s while it is
parked, correlation +0.55. A follower has to stop, so this is the evidence that it tracks the car
rather than just flying down the same street.
Row 2 is a deliberate failure: the fence has no way round, so the car escapes and tracking collapses
to 28.6% — with zero Shield overrides, because the controller now stops itself, and the zone still
never entered.

## Slide 7
PROOF
Use language as control
Identical scene, identical orange car, identical settings.
06
"an orange car"
100% of the flight within 30 m
mean separation 15.6 m
"a blue car"
20.7% within 30 m
mean separation 68.5 m
This is the control that matters. Without it, "the drone ended up near the car" could just be drift.
The colour word is verified against the pixels in the box — the detector grounds the noun,
an HSV check grounds the adjective.

## Slide 8
SAFETY
Guardrail safety
The no-fly-zone flight, before and after the controller learned about fences.
07
659 → 0
Shield overrides, after the fix
3.00 m
closest approach; stand-off is 3 m
0.0 s
inside the zone, every flight
Two layers arguing ten times a second looks exactly as unsafe as it is.
The servo asked to close on the car every tick and the Shield refused every tick. Neither changed its
mind, so the aircraft chattered against the boundary — 659 corrections in 795 ticks. The controller
now knows the geofence itself (mission data, not target data), brakes from 12 m and holds at 3 m,
while yaw keeps tracking so the target stays in view. HUD reads NFZ AHEAD — HOLDING.

## Slide 9
Q: HOW DO THEY CONNECT?
The pilot and the guardrail share one struct.
That contract is why the pilot could be replaced without touching the safety layer.
08
guardrail/models.py
class Action4D:
vx, vy # m/s, North / East
vz_up # m/s, up
yaw_rate # +clockwise
every tick, in the flight loop
raw = Action4D(...) # pilot asks
smooth = limiter(raw)
d = shield.filter(state, smooth)
drone.move_by_velocity(d.emitted)
`raw` never reaches the simulator. Only `d.emitted` flies — the guardrail is the last authority.
Case
Pilot asked for
What actually flew
Rule at risk
Guardrail agrees
vx +0.41 vy −0.62
vx +0.40 vy −0.40
none
Controller brakes itself
vy +0.74
vy +0.74 (unchanged)
none — fence 6.0 m
Guardrail overrides
vx −0.47 toward a wall
vx +0.50
clearance 4.98 < 5.0 m
Real ticks from demo/out/*/flight_log.jsonl. yaw_rate is identical in all three — the Shield never touches heading.

## Slide 10
Q: HOW DOES IT DETECT AND TURN?
From a word to a yaw command, in four steps.
09
1 · Detect
OWL-ViT takes the phrase and returns scored boxes. 34–56 ms, in its own thread.
2 · Verify the colour
HSV check inside each box. The detector grounds the noun, this grounds the adjective.
Winner is score × (0.25 + 0.75 × colour) — not score alone, which once locked onto a building.
3 · Turn
off = (cx − W/2) / (W/2) bearing = 45° × off yaw_rate = gain × bearing
The pixel offset becomes a REAL angle, because it is scaled by the camera's half-FOV.
4 · Close or back off
Box width stands in for distance: too small → forward, too large → reverse.
Scaled by cos(bearing), so it never charges while the target is off to one side.
When detection drops: COAST on the last motion (< 2 s), then SEARCH toward the side it was last seen,
then SCAN slowly. It never freezes, and never-yet-acquired counts as SEARCH rather than give-up.

## Slide 11
LIMITS
What this does not do.
Stated here so nobody discovers it during questions.
10
The noun does most of the work
"a car" alone chases city clutter and ends 51 m away. The colour check helps, but this grounds
"car", not "that particular one".
It cannot say the object is absent
With no car in the scene the raw detector still fires on ~75% of frames. Only the colour check
suppresses it.
The target is made easy, and it is a simulator
The car drives straight and parks, because turns swing it through the blind spot. The obstacle map
holds buildings only — not trees or lamp posts. One flight per condition, and no hardware yet.

## Slide 12
NEXT
Where this goes.
11
Confidence, not just position
A track-confirmation stage, so the system can report that the target is gone instead of
locking onto whatever is nearest.
A fence with a gap
Built and unit-tested — it picks the open side and refuses when there is none — but not yet
demonstrated in flight: the aircraft met street furniture the obstacle map does not contain.
Toward hardware
The guardrail already runs on any action source. The open questions are latency and camera
geometry on a real airframe.

## Slide 13
TAKEAWAY
The pilot changed completely.
The safety layer did not have to.
A 7B action model was swapped for a 153 M detector and a servo loop — a different kind of
controller entirely — and the Shield accepted it without a single change to its code or its
policy files. Across every flight in this report: no-fly zone 0.0 s, altitude escape 0.0 s.
That portability is the architectural claim, and it survived replacing the brain.
Reproduce: .\run_follow_vlm.ps1 · TUTORIAL-DEMO-FOLLOW.md